## Slide 1
Dr. Engr. M Malook Rind
Ph.D (I.T), ME (CSN), MBA (MIS), BE (CS)
CCNA, CCNP, Juniper Certified.
Professor (Computer Science)
“Information Security”
Lecture # 11

## Slide 2: Contents
Network Security Appliances and Technologies
Dr. M Malook Rind Information Security Lecture 11

## Slide 3
Network Security Appliances and Technologies
Dr. M Malook Rind Information Security Lecture 11
Different Types of Network Security Appliances
Network Security Technologies

## Slide 4: Network Security Appliances
Dr. M Malook Rind Information Security Lecture 11
All modern networks have both standard networking devices (such as switches and routers) and specialized security appliances
Security can be achieved through appliances that directly address security and by using the security features in standard networking devices
Using both standard networking devices and security appliances can result in a layered security approach which can significantly improve security.
Following appliances can be dedicated to protecting a network:
  Firewalls
  Proxy servers
  Deception instruments
  Intrusion Detection and Prevention Systems (IDS & IPS)
  Security Technologies

## Slide 5: Network Security Appliances - Firewall
Dr. M Malook Rind Information Security Lecture 11
Firewalls are designed to limit the spread of malware.
Firewalls are an important element in network security, but they fall far short of being the ultimate defense
To use firewalls effectively, you must understand the function of firewalls and know different types of firewalls and specialized firewall appliances
Appliance firewall

## Slide 6: Network Security Appliances - Firewall
Dr. M Malook Rind Information Security Lecture 11
Firewall Functions
  A firewall uses bidirectional inspection to examine both outgoing and incoming network packets.
  It allows approved packets to pass through but can take different actions when it detects a suspicious packet.
  The actions are based on specific criteria or rules; these types of firewalls are called rule-based firewalls
  Firewall rules can contain parameters such as the following:
                Source address
                Destination address
                Source port
                Destination port
                Protocol
                Direction
                Priority
                Time
                Context/URL
                Action

## Slide 7: Network Security Appliances - Firewall
Dr. M Malook Rind Information Security Lecture 11
Typical firewall rule actions

## Slide 8: Network Security Appliances - Firewall
Dr. M Malook Rind Information Security Lecture 11
Firewall Categories
  Stateful vs. stateless
        Stateful = Checks firewall rules and keeps a record of the state of the connection (sender and receiver)
        Stateless = Only checks packets based on firewall rules.
  Open source vs. proprietary (Open source = more features)
  Hardware vs. software
  Hardware = are specialized separate devices that inspect traffic (more expensive but more features).
  Software = runs as a program or service on a device, such as a computer or router.
  Host vs. appliance vs. virtual
  Host = a software firewall that runs on and protects a single device (a host). (Windows Defender Firewall)
  Appliance = is typically a separate hardware device designed to protect an entire network.
  Virtual = runs in the cloud for public cloud environment.

## Slide 9: Network Security Appliances - Proxy Servers
Dr. M Malook Rind Information Security Lecture 11
Proxies are devices in networking that act as substitutes on behalf of the primary device
A forward proxy is a computer or an application that intercepts user requests from the internal secure network and processes the requests on behalf of the user.
A reverse proxy routes requests coming from an external network to the correct internal server
A proxy server can provide a degree of protection
  It can look for malware by intercepting it before it reaches the internal endpoint.
  It can hide the IP address of endpoints inside the secure network so that only the proxy server’s IP address is used on the open Internet.

## Slide 10: Network Security Appliances - Deception Instruments
Dr. M Malook Rind Information Security Lecture 11
Deception can be used as a security defense
  By directing threat actors away from a valuable asset to something that has little or no value
Network deception can involve creating and using honeypots and sinkholes
Honeypots
  A honeypot is a computer located in an area with limited security that serves as “bait” to threat actors
  Two goals of using a honeypot:
    Deflect (away from real servers)
    Discover (revealing attack techniques)
  A honeynet is a network of honeypots set up with intentional vulnerabilities
  Sinkholes
  A sinkhole is a “bottomless pit” designed to steer unwanted traffic away from its intended destination to another device
    The goal is to deceive the threat actor into thinking the attack was successful

## Slide 11: Network Security Appliances - Intrusion Detection and Prevention Systems
Dr. M Malook Rind Information Security Lecture 11
An Intrusion Detection System (IDS) is defined as a solution that monitors network events and analyzes them to detect security incidents and imminent threats.
An Intrusion Prevention System (IPS) is defined as a solution that performs intrusion detection and then goes one step ahead and prevents any detected threats.
These security solutions protect businesses by proactively thwarting potential cybersecurity incidents.

## Slide 12: Network Security Appliances - Intrusion Detection and Prevention Systems
Dr. M Malook Rind Information Security Lecture 11

## Slide 13: Network Security Appliances - Intrusion Detection and Prevention Systems
Dr. M Malook Rind Information Security Lecture 11
IDS Operation:
  An IDS (Intrusion Detection System) monitors the traffic on a computer network to detect any suspicious activity.
  It analyzes the data flowing through the network to look for patterns and signs of abnormal behavior.
  The IDS compares the network activity to a set of predefined rules and patterns to identify any activity that might indicate an attack or intrusion.
  If the IDS detects something that matches one of these rules or patterns, it sends an alert to the system administrator.
  The system administrator can then investigate the alert and take action to prevent any damage or further intrusion.
IDS Deployment Options
Inline vs. passive IDS

## Slide 14: Network Security Appliances - Intrusion Detection and Prevention Systems
Dr. M Malook Rind Information Security Lecture 11
Classification of Intrusion Detection System:
  IDS are classified into 5 types
    Network Intrusion Detection System (NIDS): is deployed at a strategic point or points within the network, where it can monitor inbound and outbound traffic to and from all the devices on the network. Once an attack is identified or abnormal behavior is observed, the alert can be sent to the administrator.
    Host Intrusion Detection System (HIDS): run on independent hosts or devices on the network. A HIDS monitors the incoming and outgoing packets from the device only and will alert the administrator if suspicious or malicious activity is detected.

## Slide 15: Network Security Appliances - Intrusion Detection and Prevention Systems
Dr. M Malook Rind Information Security Lecture 11
    Protocol-based Intrusion Detection System (PIDS):
        A specific IDS that monitors the protocol in use.
        This system typically analyzes the HTTP or HTTPS protocol stream between your devices and the server.
        In most cases, a PIDS will go at the front end of a server.
        The system can protect your web server by monitoring inbound and outbound traffic.
    Application Protocol-based Intrusion Detection System (APIDS):
    Specializes in software app security.
    Typically associated with host-based intrusion detection systems (HIDS), APIDSs monitor the communications that occur between applications and the server.
    An APIDS is typically installed on groups of servers.
    Hybrid Intrusion Detection System:
    is made by the combination of two or more approaches to the intrusion detection system.
    In the hybrid intrusion detection system, the host agent or system data is combined with network information to develop a complete view of the network system.
    The hybrid intrusion detection system is more effective in comparison to the other intrusion detection system.

## Slide 16: Network Security Appliances - Intrusion Detection and Prevention Systems
Dr. M Malook Rind Information Security Lecture 11
Monitoring Methodologies used by IDS/IPS
Monitoring involves examining network traffic, activity, transactions, or behavior to detect security-related anomalies.
  Anomaly-based Monitoring: Detect unknown malware attacks as new malware. Machine learning is used to create a trustful activity model and anything coming is compared with that model and it is declared suspicious if not found in the model.
    Whenever activity deviates significantly from the baseline, an alarm is raised.
  Signature-based Monitoring: Detects on the basis of the already known malicious instruction sequence that is used by the malware. The detected patterns in the IDS are known as signatures.
    Signature-based IDS can easily detect the attacks whose pattern (signature) already exists in the system but it is quite difficult to detect new malware attacks as their pattern (signature) is not known. Signature database must be constantly updated.
  Behavior-based Monitoring: Attempts to overcome the limitations of both anomaly-based monitoring and signature based monitoring by being adaptive and proactive instead of reactive.
    Continuously analyzes the behavior of processes and programs on a system and alerts the user if it detects any abnormal actions
    Alerts user who decides whether to allow or block activity.
  Heuristic Monitoring: Uses experience-based techniques and attempts to answer the question “Will this do something harmful if it is allowed to execute?”

## Slide 17: Network Security Appliances - Intrusion Detection and Prevention Systems
Dr. M Malook Rind Information Security Lecture 11

## Slide 18: Network Security Appliances - Security Technologies
Dr. M Malook Rind Information Security Lecture 11
  Access technologies
Access Control List (ACL)
  ACL is made up of rules that either allow access to a computer environment or deny it.
  is a list of permissions that dictate what a user has access to and what types of operations they are allowed to do with that access.
  Two types of ACLS include:
    File system ACLs: tells the operating system which users can access the system and which privileges they are granted.
    Networking ACLs: tells the routers and switches what traffic is allowed access to the network and what type of activity is allowed.
  ACLs can also be categorized by the way they identify traffic:
    1. Standard ACLs: filter only the source address of the data packet.
    Block or allow an entire protocol suite using source IP addresses.
    2. Extended ACLs: block or allow network traffic based on a more differentiated set of characteristics that includes uses source IP, Destination IP, source port, and Destination port.

## Slide 19: Network Security Appliances - Security Technologies
Dr. M Malook Rind Information Security Lecture 11
B) Virtual Private Network (VPN)
  A VPN is a security technology that enables authorized users to use an unsecured public network (the Internet) as if it were a secure private network.
  It provides a secure, encrypted connection between two points.
  VPN creates a virtual tunnel to transfer data.
  VPN Protocols:
Internet Protocol Security (IPSec)
Layer 2 Tunneling Protocol (L2TP)
Point–to–Point Tunneling Protocol (PPTP)
SSL and TLS
Secure Shell (SSH)
SSTP (Secure Socket Tunneling Protocol)
WireGuard

## Slide 20: Network Security Appliances - Security Technologies
Dr. M Malook Rind Information Security Lecture 11
  Types of VPNs
    Site-to-Site VPN: designed to securely connect two geographically-distributed sites. It is a connection between two or more networks, such as a corporate network and a branch office network.
    Remote Access VPN: is designed to link remote users securely to a corporate network. Iddeal for organizations that need to give employees or others out-of-office access to the company network
    Personal VPN: Establishes a digital connection between your computer and a remote server owned by a VPN provider, creating a point-to-point tunnel that encrypts your personal data, masks your IP address, and lets you sidestep website blocks and firewalls on the internet.

## Slide 21: Network Security Appliances - Security Technologies
Dr. M Malook Rind Information Security Lecture 11
  2) Monitoring and managing technologies
Port Security
  Threat actors who access a network device through an unprotected ports can be blocked.
  Route security is the trust of packets sent through a router
    False route information can be injected by attackers through unprotected ports.
Packet Capture and Analysis
  Analyzing packets helps to monitor network performance and reveal cybersecurity incidents
  Monitoring traffic on switches can be done in two ways:
    A separate port TAP (test access point) can be installed
    Port mirroring (also called port spanning) allows the administrator to configure the switch to copy traffic on some or all ports to a designated monitoring port on the switch
Monitoring Services
  An external third-party monitoring service can be used to provide additional resources to assist an organization in its cybersecurity defenses such as managed SIEM platform.

## Slide 22: Network Security Appliances - Security Technologies
Dr. M Malook Rind Information Security Lecture 11
Port mirroring

## Slide 23: Network Security Appliances - Security Technologies
Dr. M Malook Rind Information Security Lecture 11
  3) Design Technologies
Network Segmentation
  Examples of network segmentation include Virtual LANs (VLANs) and a Demilitarized Zone (DMZ).
  Zero trust is a strategic initiative about networks that is designed to prevent successful attacks, it attempts to eliminate the concept of trust from an organization’s network architecture, so zero trust requires that networks be segmented.
  A network can be segmented by separating devices into logical groups by creating a Virtual LAN (VLAN), allowing scattered users to be logically grouped together.
  VLANs can be isolated so that sensitive data is transported only to members of the VLAN, this is helpful as grouping by user can be difficult because all users might not be in the same location and served by the same switch.
  A Demilitarized Zone (DMZ) is a separate network located outside secure network perimeter
  Untrusted outside users can access DMZ but cannot enter the secure network

## Slide 24: Network Security Appliances - Security Technologies
Dr. M Malook Rind Information Security Lecture 11

## Slide 25: Network Security Appliances - Security Technologies
Dr. M Malook Rind Information Security Lecture 11
  3) Design Technologies
Network Segmentation
  Other network zones

## Slide 26: Network Security Appliances - Security Technologies
Dr. M Malook Rind Information Security Lecture 11
  3) Design Technologies
B) Load Balancing
  An Load balancing is a technology that can help to evenly distribute work across a network and can allocate requests among multiple devices
  Advantages of load-balancing technology:
    A Reduces probability of overloading a single server
    Optimizes bandwidth of network computers
  Security advantages of using a load balancer:
    They can detect and stop attacks directed at a server or application
    Can also detect and prevent protocol attacks

## Slide 27
Thanks
Dr. M Malook Rind Information Security Lecture 11